## Slide 1
Arrow/Cypress Two Hour Lunch-n-Learn
Presented by your local Arrow FAE
BLE_Mesh-Two_Hour 2019
Rev 10
Notes: Aligns with BLE_Mesh-01-Tour-ModusToolbox.docx
Aligns with portion of WBT101-01-Tour from GitHub https://github.com/iotexpert/WBT101
Portions from file found linked to Documentation tab of https://www.cypress.com/products/modustoolbox-software-environment. (ModusToolbox documentation can be found on the web per the above link or in ModusToolbox in the Documentation section)
ModusToolbox™ IDE User Guide Rev *A @ https://www.cypress.com/file/455211/download
ModusToolbox™ IDE Quick Start Guide Version 1.1 @ https://www.cypress.com/file/455221/download
Eclipse IDE Survival Guide KBA225399 Rev *H @ https://community.cypress.com/docs/DOC-15617

## Slide 2
Introduction to Modus Toolbox
Subset of …
BLE_Mesh-01-Tour-ModusToolbox 2019
Notes: Aligns with BLE_Mesh-01-Tour-ModusToolbox.docx
Aligns with portion of WBT101-01-Tour from GitHub https://github.com/iotexpert/WBT101
Portions from file found linked to Documentation tab of https://www.cypress.com/products/modustoolbox-software-environment. (ModusToolbox documentation can be found on the web per the above link or in ModusToolbox in the Documentation section)
ModusToolbox™ IDE User Guide Rev *A @ https://www.cypress.com/file/455211/download
ModusToolbox™ IDE Quick Start Guide Version 1.1 @ https://www.cypress.com/file/455221/download
Eclipse IDE Survival Guide KBA225399 Rev *H @ https://community.cypress.com/docs/DOC-15617

## Slide 3
Wireless radio standards and combinations
  Wi-Fi® (802.11ac, 802.11bgn), Bluetooth (BR, EDR, BLE)
  Advanced coexistence algorithms for multi-radio (Wi-Fi + Bluetooth) platforms
Arm®-based MCUs
  PSoC® 4: Arm Cortex® M0 and M0+ devices ideal for HMI, sensor hubs, and mixed-signal subsystems
  PSoC 6: Most-flexible, low-power, dual-core Arm Cortex®-M4 and M0+ MCUpurpose-built for the IoT
WICED IoT platform provides turnkey wireless connectivity
  SDK: Simple, pre-integrated, guaranteed interoperable, continuously updated
  Ecosystem of module makers, VARs, technology partners, and OEMs deliver WICED-based end-to-end solutions
Power System
Memory System
PSoC® MCU
Wireless
Wired
USB
Wi-Fi®
NOR &
Flash
SRAM F-RAM™
NVSRAM
Analog/ PMIC
Sensors
Cypress
Actuators
UI System
CapSense®
Touchscreen
LCD Graphics
Bluetooth®
Cypress’ Portfolio of Embedded Solutions
Notes: >>Manual Section 1.1 Tour of ModusToolbox IDE
High level overview of Cypress products and major IDE tools
Take-Aways:
Cypress has three product lines: Connectivity; Processing; Memory
Cypress has three IDEs: PSoC Creator; WICED; ModusToolbox

## Slide 4
The Evolution of ModusToolbox
Single, Coherent & Familiar Design Experience
Peripheral Driver Library & Board Support Packages included
Eclipse IDE
Advanced multi-radio co-existence algorithms
Cypress SDK
PSoC MCUs
PSoC6: Arm Cortex-M4 & Cortex-M0+
Peripheral Driver Library
Integrated Security for the IoT
Wi-Fi and Bluetooth APIs & Drivers
Simple Cloud Connectivity
Eclipse IDE
Advanced Co-existence
Notes: >>Manual Section 1.1 Tour of ModusToolbox IDE
Background history of ModusToolbox
Take-Aways:
1) ModusToolbox combines features from PSoC Creator and WICED into an updated Eclipse IDE.

## Slide 5
IDE Overview
ModusToolbox based on Elcipse IDE “Oxygen” version
Quick Panel is unique to ModusToolbox, providing links for
  Device Configurator
  Middleware Selection
  Build + Program application
  SDK tools
Documentation for IDE, SDK under Help menu
Outline
Notes: >> Manual 1.1.1 First Look
Reference Section 4. IDE Description from Modus Toolbox IDE User Guide Rev *A
Take-Aways: ModusToolbox modeled after Eclipse. Quick Panel adds links to documentation and Cypress Custom Features such as Device Configurator

## Slide 6
Code Examples
20819 Code Examples (CE’s) on Cypress GitHub portal. Refer README.md file for high level details on the examples available in the repo.
20819 CE’s organized based on the kits, and further categorized in to snips and demos like in WICED Studio. Each CE has readme.txt file that provides high level CE description.
Refer to Knowledge Based (KB) article on how to download the CE’s from GitHub, and import the code examples into the IDE
Notes: Take-Aways: Examples have been developed and embedded in ModusToolbox and on GitHub now. More repositories are being developed.

## Slide 7
Device Configurator
Configure the device pins. Replaces the SuperMux Wizard from WICED Studio
Configuration settings stored in the design.modus file. Double click the file in MTB IDE to open the Configurator, or click on Configure Device in the Quick Panel
Generates configuration code under the GeneratedSource folder when changes are saved.
Launch other related configurators like Bluetooth Configurator
Notes: MTB = ModusToolBox
Open Configurator by double clicking “design.modus”
Take-Aways = Design Configurator opens a GUI to configure hardware platform specific features

## Slide 8
Bluetooth Configurator Usage
Click on GATT profile
Add “Find Me Target” profile
Final GATT database view
Notes: Take-Away: Cypress makes customizing BLE features easy

## Slide 9
BTSpy – Trace Viewer Utility to receive, decode and display protocol application and stack trace messages.
BT SDK Tools – BT Spy & Client Control
ClientControl - Host app to communicate with the embedded app to perform various functionalities, tests, exercising features, etc.
Together they allow viewing trace messages over HCI UART interface.
Launched from Quick Panel.
Reference: “ModusToolbox IDE User Guide”
Notes: Take-Aways: BT Spy and Client Control provide additional visibility to debug Bluetooth projects

## Slide 10
Intro to ModusToolbox - Summary
Newest of Cypress’ Integrated Design Environments
ModusToolbox is an Eclipse-based IDE
  Comprises unified Cypress SDK that is IDE agnostic and merges the PSoC MCU libraries and the WICED wireless libraries
  Combines PSoC Creator and WICED features and workflows into a single product catering to MCU and IoT products
  Supports both programming and debugging through OpenOCD and Segger
  WICED7 integration into combined SDK
  BT Designer Integration
GitHub
  Embracing GitHub as distribution mechanism for Example code
  Distributing more examples through SDK to use offline.
Notes: ModusToolbox is Cypress vehicle for supporting customers with key features from existing and previous tool suites

## Slide 11
Introduction to Cypress BLE Mesh
Subset of …
BLE_Mesh-02-Rev01-Tour ModusToolbox 2019

## Slide 12
BLE Basics
Wireless Personal Area Network
2.4 GHz band
40 channels with 2MHz spacing
  3 channels for advertising
  37 channels for connected communication
Short transmission bursts between periods of idle
Negotiated connection intervals for frequency of data vs power consumption
2Mbps capable with BLE 5; 1Mbps pre BLE 5
Notes: BLE is a low energy personal area network adopted by smartphones which propelled its adoption and popularity

## Slide 13
Bluetooth History
Bluetooth Spec | Year | Major Features
1.0 | 1999 | Initial standard.
1.1 | 2002 | Addition of RSSI and non-encrypted channels.
1.2 | 2003 | Adaptive Frequency Hopping (AFH); Host Control Interface (HCI); Addition of flow control and retransmission.
2.0 + EDR | 2004 | Addition of EDR (up to 3 Mbps).
2.1 + EDR | 2007 | Addition of Secure Simple Pairing (SPP) and enhanced security; Extended Inquiry Response (EIR).
3.0 + HS | 2009 | Alternative MAC/PHY (AMP); Enhanced Retransmission Mode (ERTM) and Streaming Mode (SM).
4.0 + LE | 2010 | Addition of BLE; Generic Attribute Profile (GATT); Security Manager (SM) with AES encryption.
4.1 | 2013 | Incremental software update.
4.2 | 2014 | LE secure connections with data packet length extension; Link Layer privacy; Internet Protocol Support Profile (IPSP) version 6.
5 | 2016 | LE up to 2 Mbps, or 4x range or 8x data broadcasting capacity.
5.1 | 2019 | Mesh-based model hierarchy; Angle of Arrival (AoA) and Angle of Departure (AoD) for tracking; Advertising Channel Index; GATT Cacheing
Notes: Bluetooth was the audio standard that evolved to BLE for security and power reasons

## Slide 14
BLE Mesh vs Other Mesh Technologies
1 | OSI Model – Full Stack Implementation
2 | Radio – Established technology in billions of devices
3 | Wireless Interference – Single Channel vs 3 Channels
4 | Range – 300 meters to 1 km
5 | Data Rate – Up to 2 Mbps
6 | Shorter Packets – 29 octets
7 | Power Consumption / Duty Cycle
8 | Interoperability / Certification
9 | Compatibility with Smartphones and Tablets
10 | Cost
Notes: BLE Mesh has evolved by understanding trade-offs of competing standards

## Slide 15
BLE Mesh vs Other Mesh Technologies
Notes: BLE has benefits over the current dominant Mesh Standard, ZigBee

## Slide 16
CYBT-213043-MESH BLE Mesh Evaluation Kit
CYBT-213043-MESH Kit includes
  4x CYBT-213043-Mesh evaluation boards
  4x USB cables
  Quick Start Guide
Each CYBT-213043-Mesh evaluation boards showcases
  CYW20819-based certified module, CYBT-213043-02
  Red, Green, Blue (RGB) LED
  User button
  Sensors - Ambient Light Sensor (ALS), Thermistor and PIR Motion Sensor
  1MB External Serial Flash
  On-board Programmer
Kit provides great out-of-box user experience
  Cypress iOS and Android mesh applications can be used to provision, create mesh network and control quickly and easily

## Slide 17
Cypress BLE-Mesh kits
CYBT-213043-MESH
  4 board kit
  1 user Button, RGB LED, Ambient Light Sensor
CYW920819EVB-02
  ARM-M4 w/1MB ROM, 256kB Flash,176kB SRAM
  1 user Button, 2 User LEDs
CYW920706WCDEVAL
  ARM-M3 w/848kB ROM, 352kB SRAM, 2kB NVRAM, 512kB External Serial Flash
  1 user Button, 2 User LEDs
CYW920719Q40EVB-01
  ARM-M4 w/2MB ROM, 1MB Flash, 512kB SRAM
  1 user Button, 2 User LEDs
Notes: Multiple Cypress kits available

## Slide 18
ADI Shields
CN0397 – ADI RGB light sensor
Color light recognition system
Smart agriculture applications
16-bit digitization
Low power
Arduino-compatible shield format

## Slide 19
BLE-Mesh – Mesh-Topology
Subset of …
BLE_Mesh-04-Mesh-Topology 2019
Notes: Aligns with BLE_Mesh-04-Mesh-Topology.docx
Aligns with portion of WBT101-07a-Mesh-Topology from GitHub https://github.com/iotexpert/WBT101

## Slide 20
Overview
Traditional BLE uses: Advertise to setup; Paired Connections for communication.
BLE-Mesh uses Advertise to communicate.
BLE-Mesh devices can relay messages to extend the overall communication range.
Devices in a mesh network are called “Nodes".
Devices not part of a mesh network (yet) are called "un-provisioned devices".
A mesh network can have Subnets that enable isolation of related groups of nodes.
Subnet nodes share a network key.
A node may belong to more than one subnet by having more than one network key.
Notes: >> Manual 4.1 Overview
*** Might break out discussion of Subnet or provide reference material for further reading in manual ****

## Slide 21
Node Types
Nodes can send and receive
Nodes may be one or more of:
  Relay
  GATT Proxy
  Friend
  Low Power
Notes: >> Manual 4.3 Nodes
Relay, GATT Proxy and Friend features can all be implemented on the same node. Typically, it doesn't make sense for a Low Power node to implement any of the other features as you will see in a minute.
Standard BLE Mesh networks have various types of Nodes to accommodate key aspects of applications and features:
Relays to extend coverage
Low Power for battery powered
Friends to enable Low power Nodes
Proxy to connect to common existing infrastructure

## Slide 22
Provisioning and Configuration Management
Provision – Focus on the node – Invite to join a network
  Identify & Invite
  Keys & Authentication
Configure – Focus on network – setup to receive new node
Notes: >> Manual 4.4 Provisioning and Config Mgmt
Provision a Device to become a Node and join a Network
Configure the Network to accept the Node

## Slide 23
Client Control Mesh (CCM) (Windows)
“Client Control Mesh” is an extension of the Client Control application that can be used for other WICED Bluetooth applications. It is located at:
<Install Folder>/ModusToolbox_1.1/libraries/bt_sdk-1.1/components/BT-SDK/common/apps/snip/mesh/ClientControl/Release/ClientControlMesh.exe
To use “Client Control Mesh”, program a kit that will act as an interface from the PC to the mesh devices in the network.
That kit will receive HCI commands from the PC over UART and in turn sends the appropriate messages to the mesh network.
Wired Connection to Mesh
Notes: >> Manual 4.5.2 Mesh Client for Windows

## Slide 24
Client Control Mesh (CCM) (Windows)
Locate & Run ClientControlMesh.exe
  <Install Folder>/ModusToolbox_1.1/libraries/bt_sdk-1.1/components/BT-SDK/common/apps/snip/mesh/ClientControl/Release/ClientControlMesh.exe
Connect a wired Interface
  CYW920819EVB-02 kit
  -or-
  CYBT-213043-MESH kit
Interaction will start when kit is Programmed for Mesh Functionality
Wired Connection to Mesh
Notes: >> Manual 4.5.2 Mesh Client for Windows

## Slide 25
CCM – Light Control, Models & Configuration
This application allows low-level interaction with the mesh network.
Wired Connection to Mesh
Notes: >> Manual 4.5.1 Client Control Mesh (CCM) for Windows

## Slide 26
Mesh Client (Windows 10)
Mesh Client communicates with a mesh network directly using the BLE radio of the computer.
Windows 10 based PCs have support for BLE.
The app communicates with the mesh network via a proxy.
Wireless Connection to Mesh
Notes: >> Manual 4.5.2 Mesh Client (Windows)

## Slide 27
Mesh Client (Windows 10)
Note: Latest version in BT example repository on GitHub:
https://github.com/cypresssemiconductorco/Code-Examples-BT-SDK-for-ModusToolbox/blob/master/Mesh-Peer-Apps/Windows.zip
Unzip the file and go to Windows/MeshClient/Release/x86 to find MeshClient.exe.
Wireless Connection to Mesh
Locate & Run MeshClient.exe
<Install Folder>/ModusToolbox_1.1/libraries/bt_sdk-1.1/components/BT-SDK/common/apps/snip/mesh/peerapps/Windows/MeshClient/Release/x86/MeshClient.exe
Interaction will start when a kit is Programmed for Mesh Functionality and in range of the PC
Notes: >> Manual 4.5.2 Mesh Client (Windows)

## Slide 28
Mesh Client Flow
Enter a name for your network
Click Create
Click Open
Click Scan Un-provisioned
Wait for target device to appear in the list then click Stop Scanning
  >If multiple un-provisioned devices; stop and restart until the target device appears.
Click Provision and configure
  >This step takes a few seconds – wait until complete.
Select target device in Control dropdown.
Use On/Off Get, On/Off Set, Level Get, Level Set, etc. to control your device.
Notes: >> Manual 4.5.2 Mesh Client (for Windows)

## Slide 29
Mesh Lighting App - Flow
Create a network
Select a group (ALL is created by default)
Add a device to the group
  This will take a few seconds. Wait until it completes before proceeding
Connect to the network if it doesn't happen automatically (bar will be green when connected)
Select the device
Control the device
  Note: you can control all devices simultaneously at the group level or individually at the device level
Notes: >> Manual 4.5.3 Mesh App for Android

## Slide 30
BLE-Mesh – Mesh Details
Subset of …
BLE_Mesh-05-Mesh-Details 2019
Notes: Aligns with BLE_Mesh-05-Mesh-Details.docx
Aligns with portion of WBT101-07B-Mesh-Details from GitHub https://github.com/iotexpert/WBT101

## Slide 31
Protocol Details
Concepts to understand Mesh Networks
Elements: States and Properties; State Transitions; State Binding
Scenes
Messages: Control vs Access; Ack vs UnAck; Get, Set, Status; Segmented vs Un
Addressing: Unicast; Group; Virtual
Publish and Subscribe
Fan
Element
Light
Element
Fixture Node
Notes: >> Manual 5.1 Protocol Details
Ceiling fan image from http://www.neiltortorella.com/ceiling-fan-bulb/superb-ceiling-fan-bulb-7-images-of-ceiling-fans-with-light-bulbs/
Car seat position image from YouTube https://www.youtube.com/watch?v=zwF1uR50K7o

## Slide 32
Models
Define functionality of a node
Bring together concepts of states, transitions, bindings and messages for an element
Analogous to Services in regular Bluetooth
Three categories of Models:
  Server
  Client
  Control
Model Categories
  Generic: On/Off …
  Specific: Lighting, Sensors, Time…
  Scenes: Store a collection of states
  All Bluetooth SIG defined models can be found in Mesh Model Spec.
Notes: >> Manual 5.2 Models
Image of Light Switch from http://clipartmag.com/switch-drawing#switch-drawing-36.jpg
Image of Light Bulb from icons in PowerPoint

## Slide 33
Mesh Stack Architecture
Layered Stack between User Application (top) & BLE Core Stack (bottom)
Model Layer – Implements Behaviors, Messages, States…
Foundation Model Layer – Implements Models
Access Layer – Defines format of data and Process of Information
Upper Transport Layer – Encryption / Decryption & Control including Friendship
Lower Transport Layer – Segmenting / Re-Assembling Messages
Network Layer – Handles Message Addressing. Relay and Proxy features re-direct passing messages at this Layer… back out the Bearer.
Bearer Layer – Defines Message format: Advertise, GATT….
Notes: >> Manual 5.3 Mesh Stack Architecture

## Slide 34
Security
Security is REQUIRED for Bluetooth Mesh Networks
Network, applications, and devices all have independent security that cannot be switched off.
Provisioning process has required security built in.
Mesh security protects against "replay attacks" and nodes can be removed from a network securely which prevents "trashcan attacks".
Security Keys: Network Key; Application Key; Device Key
Preventing Replay Attacks: Sequence Number; IV Index
Node Removal and Preventing Trashcan Attacks
Notes: >> Manual 5.4 Security
Security is built into Mesh networks with keys structured for various types of access

## Slide 35
BLE-Mesh – Mesh Firmware
Subset of …
BLE_Mesh-06-Mesh-Firmware 2019
Notes: Aligns with BLE_Mesh-06-Mesh-Firmware.docx
Aligns with portion of WBT101-07C-Mesh-Firmware from GitHub https://github.com/iotexpert/WBT101

## Slide 36
Firmware Architecture
Mesh and User Applications
Mesh Application files provided to interface with Mesh Networks are complete and open sourced
User Application support:
  Includes
  Configuration Variables
    Top Level Variables
    Models
    Sensors
    Properties
    Elements
    Device Configuration
Notes: >> Manual 6.1 Firmware Architecture
>> Manual 6.1.1 Mesh Application and Libraries
>> Manual 6.1.2A and 2B User Application

## Slide 37
Firmware Architecture
Mesh and User Applications
User Function Callbacks:
  Application Initialization
  Button Processing
  GATT Connection Status
  Attention Processing
  Notify Period Set
  WICED HCI Command
  Low Power Node (LPN) Sleep
  Factory Reset
Sending Messages:
  Utilize functions
Notifying Mesh Model Library:
  Notify the Mesh of local changes
Notes: >> Manual 6.1 2C User Function Callbacks
>> Manual 6.1 2D Sending Messages
>> Manual 6.1 2E Notifying Mesh Model Library of local changes

## Slide 38
Mesh Demo Starter Applications
Detailed Description of Four Applications. More available on GitHub
Light Dimmable (Server)
On Off Switch (Client)
Dimmer (Client)
Sensor Temperature (Server)
Notes: >> Manual 6.2 Mesh Demo Starter Applications

## Slide 39
BLE-Mesh – Demos
2019

## Slide 40
BLE-Mesh – Demos
The following Mesh Examples Demonstrate Cypress Tools
Light Dimmable (Server)
On Off Switch (Client)
Dimmer (Client)
Sensor Temperature (Server)
Notes: >> Manual 6.2 Mesh Demo Starter Applications
Recommend Setting up and testing a method to display Android App on screen for demo portion of tutorial.
Possible Reference @ https://fossbytes.com/android-screen-mirroring-apps-pc/

## Slide 41
Note to Presenter running the Demos
Switch presentation screen to show the software tools being used:
  ModusToolbox
  Console program TeraTerm or Putty
  Smartphone Ap using a tool such as AirDroid
Switch to show software tools

## Slide 42
Exercises: Lights, Network, Action
Program, Provision, Configure and Group using CYBT-213043-Mesh kit
Exercises use existing example, make minor modifications, then program kits.
Introduces details of Application by:
  Setting up a Mesh Network
  Finding and Provisioning Device to create Mesh Node
  Controlling the Node using the App
  Creating Groups (setup as Rooms)
  Associating Nodes with one or more Groups

## Slide 43
Exercise Ch4  Mesh with Dimmable Light
Purpose: Create small mesh network.
In ModusToolbox IDE, create a New Application for:
  Target Hardware: CYBT-213043-MESH
  Starter Application: BLE_Mesh_LightDimmable
2. Select
CYBT-213043-MESH
Notes: Previous Exercise 7A.1

## Slide 44
Exercise Ch4  Mesh with Dimmable Light
3. Select Starter Application: BLE_Mesh_LightDimmable
4. Observe the resulting File Structure
Notes: Previous Exercise 7A.1

## Slide 45
Exercise Ch4  Mesh with Dimmable Light
5. Open the file "light_dimmable.c“
6. Find where device name is assigned.
Hint: Use <ctrl> F to activate the Find/Replace pop-up, then search for “name”.
Notes: Previous Exercise 7A.1

## Slide 46
Exercise Ch4  Mesh with Dimmable Light
7. Program the project to one of the CYBT-213043-MESH kits..
Click BLE_Mesh_LightDimmable Build + Program
Observe progress bar in lower right corner and status scrolling in the Console window
“Download succeeded” will appear in the Console window when complete.
Notes: Previous Exercise 7A.1

## Slide 47
Exercise Ch4  Mesh with Dimmable Light
  8. Open a terminal window (TeraTerm, Putty or similar)
  Select the COM port hosting the Peripheral UART to see messages.
  Note: The default PUART baud rate for the mesh applications is 921600.
  Hint: If terminal emulator does not support 921600; from ModusToolbox, open the file in libraries/mesh_app_lib/mesh_app_hci.c and search for 921600. Change that value to one that is supported and rebuild/reprogram.
Notes: Previous Exercise 7A.1

## Slide 48
Exercise Ch4  Mesh Dimmable Light (Android)
9. Run the Mesh Lighting application to provision the device.
  Hint: If no devices appear after ~10 seconds, exit the app, stop/restart BLE then try again.
11. Select vertical Elipses to open drop-down
10. Observe opening screen designed by an Engineer
12. Create a unique name for your network
13. A quick confirmation will appear
Android
Notes: Previous Exercise 7A.1

## Slide 49
Exercise Ch4  Mesh Dimmable Light (Android)
14. Click
“All”
15. Click
“Add Device”
16. Create unique name for this device. Include initials and number
17. Observe “Connected to network”, “Provision Complete” then Device showing in Ap
18. Click either Green or Red Circle to turn the LED on a Device ON or OFF respectively.
Green and Red Circles in the Group section affect all Devices. The lower Circles affect a specific Device.
Android
Notes: Previous Exercise 7A.1

## Slide 50
Exercise Ch4  Mesh Dimmable Light (iOS)
For an iOS device, these screen shots provide guidance – for Android, jump back…
9. Run the Mesh Lighting application to provision the device.
  Hint: If you don't see any devices after ~10 seconds, exit the app, stop/restart BLE then try again.
10. iOS Ap may have previous Networks
11. Create a New Network
12. Observe New Network Added
13. Open New Network and add Office Group
Apple iOS
Notes: Previous Exercise 7A.1

## Slide 51
Exercise Ch4  Mesh Dimmable Light (iOS)
15. Add a device to Office Group
16. Observe the Device Provision
17. Observe New Device added to the Group
Apple iOS
Click the ON and OFF buttons and see the lights on the board change.
14. Open Group
Notes: Previous Exercise 7A.1

## Slide 52
Exercise Ch4  4.1 Mesh with Dimmable Light
19. Observe activity in the Console reacting to actions on the Ap.
Notes: Previous Exercise 7A.1

## Slide 53
Exercise Ch5  Add Lights & Modify Group
Purpose: Add lights. Associate devices to groups
Program LightDimmable application into more mesh kits.
Notes: Previous Exercise 7B.1

## Slide 54
Exercise Ch5  Lights & Group Android (Cont’d)
Provision the new LightDimmable kits.
  Repeat steps 15-17 in the previous exercise
What are some ways to identify one device in a group?
Android
Notes: Previous Exercise 7B.1 continued
Identify a device to be provisioned by either programming one at a time then provision before programming the next
Identify a provisioned device by communicating with it and observing it’s indicator or using it’s switch or sensor

## Slide 55
Exercise Ch5  Lights & Group Android (Cont’d)
3. Provision the new LightDimmable kits.
  Repeat steps 15-17 in the previous exercise for each kit
Android
Notes: Previous Exercise 7B.1 continued

## Slide 56
Exercise Ch5  Lights & Group Android (Cont’d)
4. Create two Rooms (i.e. Groups)
Android
Notes: Previous Exercise 7B.1 continued

## Slide 57
Exercise Ch5  Lights & Group Android (Cont’d)
5. Add one component to first Group / Room.
  Hint: Leave lights in group "All". Just add them to the new rooms, don't move them.
6. Select a Component
7. Add to Group (Don’t Move to Group)
8. Select the Group then OK
9. Select Group from Home Screen
10. Observe Component in Group
Android
Notes: Previous Exercise 7B.1 continued

## Slide 58
Exercise Ch5  Lights & Group Android (Cont’d)
3. Add remaining Components to Groups. Add one Component to Two Groups.
11. 2nd Node to 1st Room
12. 3rd Node to 1st Room
13. 3rd Node also to 2nd Room
14. 4th Node to 2nd Room
15. Observe 1st Room
16. Observe 2nd Room
Android
Notes: Previous Exercise 7B.1 continued

## Slide 59
Exercise Ch5  Lights & Group Android (Cont’d)
17. Toggle all lights in Group
18. Toggle lights individually
17.
17.
18.
18.
Android
Notes: Previous Exercise 7B.1 continued

## Slide 60
Exercise Ch5  Lights & Group iOS (Cont’d)
For an iOS device, these screen shots provide guidance – for Android, jump back…
15. Add a device to Office Group
16. Observe the Device Provision
17. Observe New Device added to the Group
18. Add more lights
19. Add 2nd Light and see the number.
20. Add 3rd light.
Apple iOS
Notes: Previous Exercise 7A.1

## Slide 61
Exercise Ch5  Lights & Group iOS (Cont’d)
See the new number.
Add the Last Light.
See the new number
Click the ON and OFF buttons and see the lights on the different boards change.
Click on Devices (4) to see all the provisioned lights.
Apple iOS
Notes: Previous Exercise 7A.1

## Slide 62
Exercise Ch6  6.1 Add On/Off Switch to Mesh
Purpose: Add on/off switch to mesh network to control LEDs on LightDimmable kit(s).
Remove one LightDimmable kits from the mesh network using the Android or iOS app.
Create a new application for:
  Target Hardware: CYBT-213043-MESH
  Starter Application: BLE_Mesh_OnOffSwitch
Program the project into the mesh kit.
Provision the OnOff Switch kit to your network.
Press the user button on the OnOff Switch kit to toggle the LEDs on the LightDimmable kits.
Experiment with changing the Assignment for the OnOff Switch to control different lights or rooms.
  Hint: Switches can’t be moved to different rooms, rather Assign the device or rooms that the switch will control.
Note that lights can still be controlled using the app.
Notes: Previous Exercise 7C.1
Hint: You may want to label the kits to keep track of which one is programmed with each project. Remember if you accidentally press the user button on the LightDimmable kit, it will perform a factory reset so that kit will need to be re-provisioned.

## Slide 63
Extra Credit
Exercise Ch6  6.2 Add Dimmer Switch to Mesh
Purpose: Add dimmer device to your mesh network. This new device will be able to turn the LED on/off as well as control the brightness of the LED on the LightDimmable kit. The OnOff Switch from the previous exercise will be able to control the same LED.
Remove one kit from the mesh network using the Android or iOS app.
Create a new application for:
  Target Hardware: CYBT-213043-MESH
  Starter Application: BLE_Mesh_Dimmer
Program the project into the kit.
Provision the Dimmer kit to your network.
Press the user button on the Dimmer kit to toggle the LEDs on the LightDimmable kits.
Press and hold the user button on the Dimmer kit to adjust the brightness of the LEDs.
Verify that the OnOff switch kit and the app can still control the LED.
Experiment with Assigning the Dimmer to different lights or rooms.
Notes: Previous Exercise 7C.2
Hint: You may want to label the kits to keep track of which one is programmed with each project. Remember if you accidentally press the user button on the LightDimmable kit, it will perform a factory reset.
Hint: If you hold the “Dimmer” button for longer than 15 seconds a factory reset will be performed and the Dimmer kit will no longer be associated with the mesh network.

## Slide 64
BLE-Mesh – Conclusion
2019
Notes: Summary of BLE_Chapters 00 through 06
Summary of WBT101 from GitHub https://github.com/iotexpert/WBT101

## Slide 65
BLE-Mesh – Summary / Conclusion
What did we learn
ModusToolbox – Eclipse based IDE with WICED and PSoC Creator features; Examples embedded and on GitHub
BLE Intro – High Level of what BLE is, how BLE-Mesh will compete and kits
BLE Mesh Topology – Nodes, Provisioning and Cypress’ tools
BLE Mesh Details – Protocol, Models, Stack and Security
BLE Mesh Firmware – Architecture and Starter Applications
Notes: >> Manual 6.2 Mesh Demo Starter Applications

## Slide 66
Thank You

## Slide 69
Title Slide Option 1
Screen Friendly
Creator Name
Date

## Slide 70
Title Slide Option 2
Print Friendly
Creator Name
Date

## Slide 71
Table of Contents
Welcome |  |  | Slide 1
Best Practices |  |  | Slide 2
Title Slide Options |  |  | Slides 3-4
Table of Contents |  |  | Slide 5
About Arrow |  |  | Slides 6-13
Contact Page |  |  | Slide 14
Layout Options |  |  | Slides 15-19
Break Page Options |  |  | Slides 20-21
Closing Page |  |  | Slide 22

## Slide 72
Divider Slide Option 1
Screen Friendly

## Slide 73
Divider Slide Option 1
Screen Friendly

## Slide 74
Divider Slide Option 2
Print Friendly

## Slide 75
Divider Slide Option 2
Print Friendly

## Slide 76
About Arrow
The following are easily insertable plug-and-play slides and speaker notes to use in any of your PowerPoint presentations.
Note: Prior to using any of these slides, be sure you are using the most current version
by visiting the TEMPLATES folder in ARROW BRAND CONNECT - BrandConnect.arrow.com.

## Slide 77
Five Years Out
is the tangible future where what’s possible meets what’s practical.
Notes: Notes:
Five Years Out is the tangible future. And the people who live and work there know that new technologies, new materials, new ideas and new electronics will make life not only different, but better.
Not just cheaper, but smarter. Not just easier, but more inspired.
Five Years Out is a way of thinking that is reserved for a special group of people. Engineers, inventors, planners, managers, our customers, us. Anyone who is thinking about the next great innovation. And then the one after that.
Five Years Out is not 15 or 20 years from now, because that’s science fiction. And it’s not tomorrow, because tomorrow is practically yesterday. It is that special place in the very tangible future where what’s possible meets what’s practical.
Living in the world of Five Years Out enables us to help our customers and partners stay ahead of what’s ahead, thus helping them to define this future of tangible possibility.

## Slide 78
It’s likely you’ve already
interacted with Arrow
at least FIVE times.
If it takes a charge or sends
a signal, chances are
Arrow was a part of building it.
By The Time You’ve Had Your Morning Coffee…
Notes: Notes:
The work Arrow does goes into everything from cars to coffee makers. Smart phones, tablets, video games, refrigerators, kiosks and cable boxes.
Whether it’s amazing or mundane, something you’ve never seen before or the things you can’t live without—you name it. If it takes a charge, chances are, it was built with Arrow.
When you think about the world of Five Years Out…
Arrow is helping design it.
Build it.
Source it.
Even pay for it.

## Slide 79
Inspiration Fuels Innovation
Arrow designed and built a semi-autonomous car, SAM Car, that is enabling paralyzed former IndyCar racer Sam Schmidt to realize his dream of driving again—using only the motions of his head—and to inspire millions of others with physical impairments.
Notes: Notes:
In June 2013, engineers and medical researchers joined forces to work toward a common vision—modifying a car to be safely driven at speed by head movements for a quadriplegic race driver. This is a Semi-Autonomous Motorcar. We call it SAM.
The SAM car is designed to restore independence, control and a sense of accomplishment to a qualified disabled driver. The technology breaks down barriers and opens new physical and emotional horizons. With a little help, we all can be the drivers of our own lives.
In the project's first year, innovators at Arrow Electronics, Ball Aerospace & Technologies Corp., Falci Adaptive Motorsports and the Air Force Research Laboratory integrated separate steering, acceleration and braking controls into a seamless system. They transformed what seemed like an impossible dream into reality—and they did it in less than a year.
  “Our objective was never only how fast Sam Schmidt can drive on a racetrack. It has always been about designing a car that a quadriplegic can really drive and maybe change the world for many people.”
  -Chakib Loucif, VP of Engineering, Arrow
http://community.arrow.com/sam/

## Slide 80
Corporate Social Responsibility
Health & Medicine
Technology Innovation
Communities
Environment
Education
Employee Engagement
Notes: Notes:
Arrow’s dedicated Corporate Social Responsibility program helps guide today’s innovators to a better tomorrow—transforming their ideas into real and influential achievements that will help people and the communities in which Arrow works.
Education: Supporting promising technology and engineering innovators in K-12 schools through various community partnerships.
Environment: Committed to making the world a better place by recycling and repurposing technology equipment, reducing electronic waste and supporting green community projects.
Communities: Engagement in innovative social initiatives that bring support and technology to the community.
Technology Innovation: Partnering with incubators, accelerators and competitions to give aspiring inventors a platform to turn their ideas into real innovations.
Health & Medicine: Semi-Autonomous Motorcar (SAM) was created to help and inspire disabled driver, Sam Schmidt – and millions of people like him.
Employee Engagement: Empowering Arrow employees to engage in their communities and make the world a better place now and Five Years Out.
Additional Info:
  “Arrow is committed to developing innovative technologies and programs that help change people’s lives. Our CSR and sustainability programs continue to demonstrate Arrow’s commitment to working Five Years Out”
  Mike Long, Chairman, President and CEO, Arrow
Arrow’s CSR website: http://community.arrow.com/activities/
Employee Engagement & Grant Programs: http://www.planetarrow.com/global/charitable_giving/G000066

## Slide 81
DigiTruck and Close the Gap
In August 2015, Arrow and Close the Gap deployed the first DigiTruck, a mobile classroom that can operate off-the-grid, at the Tuleeni Orphanage in a Tanzanian village on the southern slope of Mount Kilimanjaro.
Notes: Notes:
The DigiTruck is a mobile classroom or clinic that can operate off-grid in remote areas. The unit, built from a 40-foot steel cargo container, is triple insulated to protect against tropical heat and reinforced to deter vandalism. Energy-saving technologies include LED interior lighting and rooftop solar that can power the unit for two days. Added electronics include refurbished laptops, mobile devices, an LED flat screen monitor, a printer, two routers and two solid state drives. The entire unit is fitted to a commercial truck and trailer. Arrow also installed basketball courts at the orphanage with a non-profit called Hoops of Hope. Tuleeni teachers are using the classroom to teach 80 secondary school students how to use a computer, as well as online lessons in reading, math, English and other academic subjects. Arrow employees, encouraged by a company match, have donated their own funds to sponsor the education of Tuleeni children in 2016. Those funds have helped to provide internet service, a playground, tablets and students scholarships.
This Brussels-based nonprofit helps Arrow bridge the digital divide in developing nations by distributing refurbished computers and other equipment to schools, clinics and micro-finance organizations, as well as establishing environmentally responsible e-waste facilities. Since 2004, our partnership has processed 500,000 computers and other devices from companies and reached more than 1.5 million new users, mostly in Africa.

## Slide 82
Layout Options
The following slides are examples of the easily editable templates.
For more template options, click on the “NEW SLIDE” button under the “HOME” tab
and select the desired template from the dropdown menu.

## Slide 83
One Column With Subheader Slide Example
Insert a new slide for more layout options.
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore magna aliqua.
Ut enim ad minim veniam, quis nostrud exercitation ullamco laboris nisi ut aliquip ex ea commodo consequat. Duis aute irure dolor in reprehenderit in voluptate velit esse cillum dolore eu fugiat nulla pariatur.
Excepteur sint occaecat cupidatat non proident, sunt in culpa qui officia deserunt mollit anim id est laborum. Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod.

## Slide 84
Two Column With Subheader Slide Example
Insert a new slide for more layout options.
Sed ut perspiciatis unde omnis iste natus error sit voluptatem accusantium doloremque laudantium, totam rem aperiam, eaque ipsa quae ab illo inventore veritatis et quasi architecto beatae vitae dicta sunt explicabo.
Ratione voluptatem sequi nesciunt. Neque porro quisquam est, qui dolorem ipsum quia dolor sit amet.
Exercitation ullam corporis suscipit.

## Slide 85
Chart: Pie Chart Title
| 1st Qtr | 2nd Qtr | 3rd Qtr | 4th Qtr
Sales | 8.2 | 3.2 | 1.4 | 1.2
Sed ut perspiciatis unde omnis iste natus error sit voluptatem accusantium doloremque laudantium, totam rem aperiam, eaque ipsa quae ab illo inventore veritatis et quasi architecto beatae vitae dicta sunt explicabo. Nemo enim ipsam voluptatem quia voluptas sit aspernatur aut odit aut fugit, sed quia consequuntur magni.
Ratione voluptatem sequi nesciunt. Neque porro quisquam est, qui dolorem ipsum quia dolor sit amet, consectetur, adipisci velit.
2/3 Two Column Slide Example

## Slide 86
Chart: 
| Category 1 | Category 2 | Category 3 | Category 4
Series 1 | 4.3 | 2.5 | 3.5 | 4.5
Series 2 | 2.4 | 4.4 | 1.8 | 2.8
Series 3 | 2 | 2 | 3 | 5
Comparison Slide Example
Comparison Title Comparison Title
Chart: 
| Category 1 | Category 2 | Category 3 | Category 4
Series 1 | 2.9 | 3.5 | 2.8 | 4.5
Series 2 | 3.2 | 4.8 | 2.4 | 2.8
Series 3 | 1.5 | 4 | 3 | 3

## Slide 87
Thank You

## Slide 88
Appendix

## Slide 89
Create, Make and Manage Technology
Solution Architecture & Design
Design new devices, components or finished products
Take existing solutions to the next level
Minimize design cycles to speed your time to market
Prototype to Scale
Prototyping and testing services
Get your board, component or device certified
Routes to Market
Create lead gen programs and new routes to market that boost revenue and maximize business opportunities
Put designs into production quickly with turnkey manufacturing solutions
Meet the demand for short lead times with renowned global supply chain and logistics support
Hardware & Software Integration
Device-level integration
Large-scale systems integration
Cloud Security & Analytics
Create cloud solutions unique to your industry, company, and customers
Turn data into insight, and insight into action